## Slide 1: Embedded Indoor Positioning System
Student:
Alistar Stefan
Project Coordinator:
SL.dr.ing Harja Gabriel

## Slide 2: Contents
Motivation
Objectives
Ultra wide-band
Hardware implementation
Software & testing
Trilateration
Results
Conclusion

## Slide 3: Motivation
GPS only works outdoors
The need for a cost-effective and accurate IPS
Answering a growing demand in:
  Factories – determining location of robots
  Medical domain – monitoring sick patients
  Emergency situations – guiding firemen inside buildings
  Human logistics – guiding people in airports

## Slide 4: Objectives
Design a circuit to enable transmitting and receiving distances
Design a custom PCB for the components
Use dedicated software to enable ranging between devices
Enable trilateration for determining a device position
Show coordinates in real-time using a GUI like MATLAB
Further calibrate the antennas

## Slide 5: Ultra Wide-band (UWB)
Wireless communication protocol that uses radio waves
Used by U.S. military for decades, popularized in 2019
Time-of-Flight and Received-Signal-Strength
Frequency range: 3.1-10.6 GHz
https://www.everythingrf.com/community/what-is-ultra-wide-band-uwb-technology

## Slide 6: Hardware implementation

## Slide 7: Decawave’s DWM1000
Enables UWB communication
SPI protocol
Data rates of up to 6.8 Mbps
Up to 64 MHz clock frequency
10 cm accuracy and range of up to 290m in LoS and 35m in NLoS
https://www.tme.eu/ro/details/dwm1000/module-rf/decawave/

## Slide 8: Wemos D1 Mini & additional components
Wemos D1 Mini: microcontroller used to process data received from DWM
Powerful ESP8266-based board: 80/160MHz, 4MB flash memory
Uses SPI protocol to communicate with the DWM module
3.3 V regulator for powering the DWM via a Wemos pin
10 kΩ pull-down resistor linked to IRQ pin to prevent sporious interrupts
https://www.wemos.cc/en/latest/d1/d1_mini.html

## Slide 9: Circuit design
SPI pins:
  CS (chip-select): to activate the SPI
  CLK (Clock): tells the receiver when to sample the bits
  MOSI & MISO (Master Out Slave In & Master In Slave Out): input/output signals
3.3V & GND pins
IRQ
RST

## Slide 10: PCB
Designed respecting the circuit
Used Autodesk EAGLE and Fusion360
Compact: 5.6x3 cm
Respected antenna placement

## Slide 11: Software & Testing

## Slide 12: Arduino IDE
Dedicated software library
Calibration capabilities
Ability to customize DWM configuration

## Slide 13: Testing & Algorithm used
In order to obtain the user position, 4 devices were built (3 anchors and 1 tag) to enable the trilateration algorithm
Steps:
Check connectivity with the DWM
Implement two-way ranging
Implement trilateration

## Slide 14: Trilateration
= User coordinates

## Slide 15: Results
Achieved an accuracy of 10-20 cm in Line-of-Sight
Received consistent results, with rare signal loss scenarios
Works outdoors with a range > 100m

## Slide 16: Conclusion
Designed a cost-effective Indoor Positioning System
Built a compact PCB
Achieved precision of 10-20 cm